## Slide 1: Near and Far
procedure is also called functions or sub routines. A procedure is a collection of instructions that perform some specific activity when executed in a sequence.
whenever we need to execute the instructions mentioned in the procedure, we can simply make a CALL to it.

## Slide 2: Near and Far
The Syntax for a procedure is as follows:
Procedure_name PROC [near / far]
Instruction 1
Instruction 2
- - - - - - - - - -
- - - - - - - - - -
Instruction n
Procedure_name ENDP

## Slide 3: Near procedure
1. A near procedure refers to a procedure which is in the same code segment from that of the call instruction
2. It is also called intra-segment procedure
3 A near procedure call replaces the old IP with new IP.
4. The value of old IP is pushed on to the stack.
SP=SP-2
5. Less stack locations are required
6. Procedure is inside Code Segment
7.Uses keyword near
8.Syntax:- CALL near_procedure_name
9. Example :- Call Delay

## Slide 4: Far Procedure
1. A far procedure refers to a procedure which is in the different code segment from that of the call instruction.
2. It is also called inter-segment procedure call
3. A far procedure call replaces the old CS:IP pairs with new CS:IP pairs
4. The value of the old CS:IP pairs are pushed on to the stack SP=SP-2
5. More stack locations are required 6. Procedure is outside Code Segment 7. Uses keyword FAR
8. Example :- Call FAR PTR Delay 9. Syntax:- CALL far_procedure_name

## Slide 5: Proc
PROC is a keyword to define that the set of instructions enclosed by the given name is a procedure. It is used in the starting instruction whenever we define a procedure.

## Slide 6: ENDP
ENDP keyword defines that the body of the procedure has been ended. All the instructions lying between these two keywords are the instructions that belong to the procedure and will be executed whenever a CALL to the procedure is made.

## Slide 7: RET
At the end of the procedure, the RET instruction is used. This instruction will cause the execution to be transferred to the program from which the call to the procedure was made.