## Slide 1: Memory Virtualization
Memory management in OS
  Traditionally, OS fully controls all physical memory space and provide a continuous addressing space to each process.
  In server virtualization, VMM should make all virtual machines share the physical memory space without knowing the fact.
Goals of memory virtualization :
  Address Translation
    Control table-walking hardware that accesses translation tables in main memory.
  Memory Protection
    Define access permission which uses the Access Control Hardware.
  Access Attribute
    Define attribute and type of memory region to direct how memory operation to be handled.

## Slide 6: Memory Architecture
Memory Management Unit (MMU)
  What is MMU ?
    A computer hardware component responsible for handling accesses to memory requested by the CPU.
    Its functions include translation of virtual addresses to physical addresses, memory protection, cache control, bus arbitration and etc.
  What is PTBR ?
    Page Table Base Register (PTBR) is a register point to the base of page table for MMU.

## Slide 7: Memory Architecture
Translation Lookaside Buffer (TLB)
  What is TLB ?
    A CPU cache that memory management hardware uses to improve virtual address translation speed.

## Slide 8: Memory Virtualization
Memory virtualization architecture

## Slide 9: Memory Virtualization
The performance drop of memory access is usually unbearable. VMM needs further optimization.
VMM maintains shadow page tables :
  Direct virtual-to-physical address mapping
  Use hardware TLB for address translation

## Slide 10: Shadow Page Table
Map guest virtual address to host physical address
  Shadow page table
    Guest OS will maintain its own virtual memory page table in the guest physical memory frames.
    For each guest physical memory frame, VMM should map it to host physical memory frame.
    Shadow page table maintains the mapping from guest virtual address to host physical address.
  Page table protection
    VMM will apply write protection to all the physical frames of guest page tables, which lead the guest page table write exception and trap to VMM.

## Slide 11: Shadow Page Table
How does this technique work ?
  VMM should make MMU virtualized
    VMM manages the real PTBR and a virtual PTBR for each VM
    When guest OS is activated, the real PTBR points to a shadow page table
    When guest OS attempts to modify the PTBR, it will be intercepted by VMM for further emulation

## Slide 12: Shadow Page Table
Construct shadow page table
  Guest OS will maintain its own page table for each process.
  VMM maps each guest physical page to host physical page.
  Create shadow page tables for each guest page table.
  VMM should protect host frame which contains guest page table.
Write protection

## Slide 13: Shadow Page Table
Implement with PTBR :
  For example, process 2 in guest OS want to access its memory whose page number is 1.

## Slide 14: Shadow Page Table
Shadow page table operations :
Process
Page Table
Shadow
Page Table
Process
Page Table
Shadow
Page Table
Virtual PTPR
Real PTPR
Guest OS
VMM
Corresponding mapping table
Context switch
Switch the pointer to new location
Process
Page Table
Shadow
Page Table
New process
Create new shadow page table mapping to new process
Access
Page fault !
Load !

## Slide 15: Other Issues
Page fault and page protection issue
  When a physical page fault occurs, VMM need to decide whether this exception should be injected to guest OS or not.
    If the page entry in the page table of guest OS is still valid, VMM should prepare the corresponding page and not inject any exception to guest OS.
    If the page entry in the page table of guest Os is invalid either, then VMM should directly inject the virtual page fault to guest OS.
  When guest OS want to modify its page tables, VMM need to intercept this operation.
    When guest OS reload PTBR, CPU will trap to VMM due to the Ring Compression nature.
    VMM will walk the page table of guest OS and modify the related shadow page table to make MMU get host physical address.

## Slide 16: Memory Virtualization
Shadow page table
Hardware assistance

## Slide 17: Hardware Solution
Difficulties of shadow page table technique :
  Shadow page table implementation is extremely complex.
  Page fault mechanism and synchronization issues are critical.
  Host memory space overhead is considerable.
But why we need this technique to virtualize MMU ?
  MMU do not first implemented for virtualization.
  MMU is knowing nothing about two level page address translation.
Now, let us consider hardware solution.

## Slide 18: Extended Page Table
Concept of Extended Page Table (EPT) :
  Instead of walking along with only one page table hierarchy, EPT technique implement one more page table hierarchy.
    One page table is maintained by guest OS, which is used to generate guest physical address.
    The other page table is maintained by VMM, which is used to map guest physical address to host physical address.
  For each memory access operation, EPT MMU will directly get guest physical address from guest page table, and then get host physical address by the VMM mapping table automatically.

## Slide 19: Extended Page Table
Memory operation :
8
9
6
4
7
8
Data

## Slide 20: Memory Virtualization Summary
Software implementation
  Memory architecture
    MMU (memory management unit)
    TLB (translation lookaside buffer)
  Shadow page table
    MMU virtualization by virtual PTBR
    Shadow page table construction
    Page fault and page table protection
Hardware assistance
  Extended page table
    Hardware walk guest and host page table simultaneously

## Slide 21: IO Virtualization
Overview
Device Model
Hardware Assistance

## Slide 22: IO Virtualization
Goal :
  Share or create IO devices for virtual machines.
Two types of IO subsystem architecture :
  Port Mapped IO
    Port-mapped IO uses a special class of CPU instructions specifically for performing IO.
  Memory Mapped IO (MMIO)
    Memory Mapped IO uses the same address bus to address both memory and IO devices, and the CPU instructions used to access the memory are also used for accessing devices.
Traditional IO techniques :
  Direct memory Access (DMA)
  PCI / PCI Express

## Slide 23: Port Mapped IO
IO devices are mapped into a separate address space
  IO devices have a separate address space from general memory, either accomplished by an extra “IO" pin on the CPU's physical interface, or an entire bus dedicated to IO.
  Generally found on Intel microprocessors, specifically the IN and OUT instructions which can read and write one to four bytes (outb, outw, outl) to an IO device.
Pros & Cons
  Pros
    Less logic is needed to decode a discrete address.
    Benefits for CPUs with limited addressing capability.
  Cons
    More instructions are required to accomplish the same task.
    IO addressing space size is not flexible.

## Slide 24: Memory Mapped IO
IO devices are mapped into the system memory map along with RAM and ROM.
  To access a hardware device, simply read or write to those 'special' addresses using the normal memory access instructions.
Pros & Cons
  Pros
    Instructions which can access memory can be used to operate an IO device.
    Operate on the data with fewer instructions.
  Cons
    Physical memory addressing space must be shared with IO devices.
    The entire address bus must be fully decoded for every device.

## Slide 25: Direct Memory Access
What is DMA ?
  Allow certain hardware subsystems within the computer to access system memory for reading and/or writing independently of the central processing unit.
Two types of DMA :
  Synchronous DMA
    The DMA operation is caused by software.
    For example, sound card driver may trigger DMA operation to play music.
  Asynchronous DMA
    The DMA operation is caused by devices (hardware).
    For example, network card use DMA operation to load data into memory and interrupt CPU for further manipulation.

## Slide 26: PCI & PCI Express
What is PCI ?
  PCI (Peripheral Component Interconnect) is a computer bus for attaching hardware devices.
  Typical PCI cards used include :
    Network cards, sound cards, modems
    Extra ports such as USB or serial, TV tuner cards and disk controllers.
What is PCI Express ?
  PCIe is a computer expansion card standard designed to replace the older PCI, PCI-X, and AGP standards.
  Its topology is based on point-to-point serial links, rather than a shared parallel bus architecture.

## Slide 27: PCI & PCI Express
PCI based system build in a tree topology
  PCI bus
    Parallel connect devices and bridges
  PCI-PCI Bridge
    Connect two PCI buses
    Become the root of lower bus
  PCI-ISA Bridge
    Connect to conventional ISA device

## Slide 28: PCI & PCI Express
PCIe based system build in a point to point architecture
  Root Complex
    Similar to a host bridge in a PCI system, the root complex generates transaction requests on behalf of the processor, which is interconnected through a local bus.
  Switch
    Connect endpoint devices or other switches
  Endpoint Device
    Physical PCIe devices
    Legacy PCI devices
  PCI Express Bridge
    Connect to other legacy subsystems

## Slide 29: IO Virtualization
Implementation Layers :
  System call
    The interface between applications and guest OS.
  Driver call
    The interface between guest OS and IO device drivers.
  IO operation
    The interface between IO device driver of guest OS and virtualized hardware ( in VMM ).

## Slide 30: IO Virtualization
In system call level :
  When an application invokes a system call, the system call will be trapped to VMM first.
  VMM intercepts system calls, and maintains shadowed IO system call routines to simulate functionalities.
  After simulation, the control goes back to the application in gust OS.

## Slide 31: IO Virtualization
In device driver call level :
  Adopt the para-virtualization technique, which means the IO device driver in guest OS should be modified.
  The IO operation is invoked by means of hyper-call between the modified device driver and VMM IO component.

## Slide 32: IO Virtualization
In IO operation level, two approaches :
  Memory mapped IO
    Loads/stores to specific region of real memory are interpreted as command to devices.
    The memory mapped IO region is protected.
  Port mapped IO
    Special input/output instructions with special addresses.
    The IO instructions are privileged .
Due to the privileged nature, these IO operations will be trapped to the VMM.

## Slide 33: IO Virtualization
Overview
Device Model
Hardware Assistance

## Slide 34: Device Model
Focus on IO operation level implementation.
  This is an approach of full virtualization.
Logic relation between guest OS and VMM :
  VMM intercepts IO operations from guest OS.
  Pass these operations to device model on a running platform.
  Device model needs to emulate the IO operation interfaces.
    Port mapped IO
    Memory mapped IO
    DMA
    ... etc.

## Slide 35: Device Model
Two different implementations of device model :
  Device model is implemented as part of VMM.
  Device model is running in user space as a stand alone service.
Type 1 Virtualization
Type 2 Virtualization

## Slide 36: Device Model
IO virtualization flow
  Initialization – device discovery
    VMM will make guest OS discover the virtualized IO devices.
    Then guest OS will load the corresponding device driver.
  Operation – access interception
    When guest OS executes IO operations, VMM will intercept those accesses.
    After virtual device operations, VMM returns the control to guest OS.
  Virtualization – device virtualization
    Device model should emulate the real electronic logic to satisfy all device interface definition and its effects.
    VMM may share physical devices to all virtual machines.

## Slide 37: Device Discovery
Virtualize physical bus devices
  Non-enumerable physical device
    These devices have their own hard-coded numbers.
    VMM should setup some status information on the virtual device ports.
    For example, PS/2 keyboard and mouse.
  Enumerable physical device
    These devices defined a complete device discover method.
    VMM have to emulate not only the device itself, but the bus behavior.
    For example, PCI or PCI express devices.
Virtualize non-exist devices
  VMM must define and emulate all functions of these devices
    VMM may define them as either non-enumerable or enumerable devices.
    Guest OS needs to load some new drivers of these virtual devices.

## Slide 38: Access Interception
After virtual device discovered by guest OS, VMM has to intercept and control all the IO operations from guest OS.
Port mapped IO operation
  Direct device assignment
    VMM should turn ON the physical IO bitmap.
    All the IO instructions (IN/OUT) from guest OS will be directly performed onto hardware without VMM intervention.
  Indirect device assignment
    VMM should turn OFF the physical IO bitmap.
    All the IO instructions from guest OS will be intercepted by VMM and forward to physical hardware.

## Slide 39: Access Interception
Memory mapped IO operation
  Direct device assignment
    VMM should use the shadow page table to map IO device addressing space of guest OS to the space of host.
    Then all the IO operations from guest OS will not be intercepted.
  Indirect device assignment
    VMM should make the all entries of the IO device addressing space in the shadow page table to be invalid.
    When guest OS access those addressing space, it will introduce the page fault which trap CPU to VMM for device emulation.
DMA mechanism
  Address remapping
    Because the device driver in the guest OS does not know the host physical address, VMM needs to remap the DMA target automatically when intercepting guest OS.

## Slide 40: Device Virtualization
IO device types :
  Dedicated device
    Ex : displayer, mouse, keyboard …etc.
  Partitioned device
    Ex : disk, tape …etc
  Shared device
    Ex : network card, graphic card …etc.
  Nonexistent physical device
    Ex : virtual device …etc.

## Slide 41: Device Virtualization
Dedicated device
  Do not necessarily have to be virtualized.
  In theory, requests of such device could bypass the VMM.
  However, they are handled by the VMM first since OS is running in user mode.
Partitioned device
  Be partitioned into several smaller virtual devices as dedicated to VM.
  VMM translates address spaces to those of the physical devices.

## Slide 42: Device Virtualization
Shared device
  Should be shared among VMs.
  Each VM has its own virtual device state.
  VMM translates requests from a VM to physical device .
Nonexistent physical device
  Virtual device “attached” to a VM for which there is no corresponding physical device.
  VMM intercepts requests from a VM, buffers it and interrupts other VMs.

## Slide 43: Performance Issues
When considering performance, two major problems :
  How to make guest OS directly access IO addresses ?
    Other than software approaches discussed above, we can make use of the hardware assistance (Intel EPT technique in memory virtualization) to map IO addresses from host to guest directly without software overhead.
  How to make DMA directly access memory space in guest OS ?
    For the synchronous DMA operation, guest OS will be able to assign the correct host physical memory address by EPT technique.
    For the asynchronous DMA operation, hardware must access memory from host OS which will introduce the VMM intervention.

## Slide 44: IO Virtualization
Overview
Device Model
Hardware Assistance

## Slide 45: Hardware Solution
Difficulty :
  Software cannot make data access directly from devices.
Tow hardware solutions :
  Implement DMA remapping in hardware
    Remap DMA operations automatically by hardware.
    For example, Intel VT-d .
  Specify IO virtualization standards of PCI Express devices
    Implement virtualizable device with PCI Express interface.
    For example, SR-IOV or MR-IOV.

## Slide 46: Intel VT-d
Add DMA remapping hardware component.
Software Approach
Hardware Approach

## Slide 47: IO Virtualization Progress
Software based sharing
  Implement virtualization by VMM software stack.
  Advantage
    Full virtualization without special hardware support.
  Disadvantage
    Significant CPU overhead may be required by the VMM.

## Slide 48: IO Virtualization Progress
Hardware direct assignment
  Implement virtualization with Intel VT-x and VT-d supports.
  Advantage
    Data access bypass VMM.
    Improve IO performance.
  Disadvantage
    Dedicate physical device assignment limit the system scalability.

## Slide 49: IO Virtualization Progress
New industrial standard
  Instead of implementing virtualization in CPU or memory only, industry com up with new IO virtualization standard in PCI Express devices.
  Advantages
    Fully collaboration with physical hardware devices.
    Improve system scalability.
    Improve system agility.
  Disadvantages
    IO devices must implement with new specification.

## Slide 50: Single Root – IO Virtualization
What is SR-IOV ?
  The PCI-SIG Single Root I/O Virtualization and Sharing (SR-IOV) specification defines a standardized mechanism to create natively shared devices.
Basic components :
  Physical Functions (PFs):
    These are full PCIe functions that include the SR-IOV Extended Capability.
    The capability is used to configure and manage the SR-IOV functionality.
  Virtual Functions (VFs):
    These are “lightweight” PCIe functions that contain the resources necessary for data movement but have a carefully minimized set of configuration resources.

## Slide 51: Single Root – IO Virtualization
SR-IOV works with VMM :
  VMM
    An SR-IOV-capable device can be configured to appear in the PCI configuration space as multiple functions.
  VM
    The VMM assigns one or more VFs to a VM by mapping the actual configuration space the VFs to the configuration space presented to the virtual machine by the VMM.

## Slide 52: IO Virtualization Summary
IO subsystem architecture
  Port Mapped IO vs. Memory Mapped IO
  Direct Memory Access (DMA)
  PCI / PCI Express
IO virtualization
  Three implementation layers
  IO virtualization paradigm with device model
Hardware assistance
  DMA remapping hardware
  Single Root – IO Virtualization specification